## Slide 1
End-to-End Learning of Driving Models with Surround-View Cameras and Route Planners
    Simon Hecker, Dengxin Dai, and Luc Van Gool
    Computer Vision Lab, ETH Zurich
    Dataset & Code
  Experimental Results
  Motivation
  This work is funded by Toyota Motor Europe via the project TRACE-Zurich
  Dataset
Dataset:
60 Hours of driving.
Diverse weather conditions, day/night time and road situations (city, countryside, highway).
Sensors:
8 x GoPro Hero 5 cameras @ 60Hz with 1080p and full 360 degree coverage.
TomTom and OpenStreetMap route planning representations.
Low-level CAN bus maneuver recording including steering wheel angle and vehicle speed.
GPS & IMU odometry.
Overall Performance
Ablation Study
Surround-view Cameras
Previous methods only use a front-facing camera
Surround-view cameras mimic side-view and rear-view mirrors, vital for learning driving models
Map (Route Planner) is important for navigation, but not exploited in published work for driving models
  Method
Implementation Details:
Learning to drive via imitation learning. Predict human driving maneuver (steering wheel angle and vehicle speed) for a diverse set of maneuvers based on video data and route planning data.
Learning driving models in a fully end-to-end manner: resnet34 as visual encoder, two fully connected regression networks for steering angle and vehicle speed prediction.
Simultaneous learning of control via normalized maneuver labels.
TomTom
OSM
Learning Details
We propose learning driving models in real world settings with a `complete’ sensor configuration
Using historical steering angle ,
historical speed , historical vehicle trajectory , video
data , planned route to predict future speed ,
and steering angle
Map helps significantly, esp. for steering prediction
TomTom route planner outperforms OSM planner
Multiple cameras help esp. for low-speed, city driving and driving at intersections